## Slide 1: Structural Sizing of an Aircraft Wing Structure
Alfiyandy Hariansyah (21023691)
mahariansyah@connect.ust.hk
6-Nov-2025
MECH5930 Term-Project Proposal Presentation
DEPARTMENT OF MECHANICAL AND AEROSPACE ENGINEERING
THE HONG KONG UNIVERSITY OF SCIENCE AND TECHNOLOGY

## Slide 2: Introduction: aircraft wing structure
An aircraft wing structure must withstand various loads:
  Aerodynamics
  Self-weight
  Operational loads (gust, maneuver, etc.)
Main components:
  Outer skin: transfer aero load
  Spars: resist bending and shear
  Ribs: maintain airfoil shapes
  Stringers: handle torsions

## Slide 3: Introduction: structural sizing
Structural sizing: an optimization process determining the optimal dimensions for the structures (e.g., skin thickness, spar cross-sections, rib placement)
FSI: fluid structure interaction
One-way FSI: FEA and CFD are not coupled, sizing iteration is only with FEA
Two-way FSI: FEA and CFD are coupled, sizing iteration is with both CFD and FEA

## Slide 4: Problem description
The wing geometry has not been finalized. The following is just for illustration purposes (from MDO Benchmark case, based on Boeing 717 wings). Only skins, ribs, and spars will be modelled. Stringers are not modelled.

## Slide 5: Governing Equations and Boundary Conditions
FEA: Linear Elasticity
Boundary Conditions
Fixed support at wing root, and pressure from CFD, p(x), is applied to the wing skin.
CFD: Compressible Navier-Stokes
Reynolds-Averaged Navier Stokes

## Slide 6: Proposed plans
The project only covers one-way FSI with manual sizing process. If time permits, two-way FSI with numerical optimization algorithm will be pursued.
Tools
  CFD: Ansys Fluent
  FEA: Ansys Mechanical
Metrics of interest
  Structural mass , wing tip deflection , maximum von Mises stress
  Factor of Safety: , where is the material yield strength
  Strength-to-weight ratio:
  The sizing process will maximize this SFW ratio.
Assumptions
  Load case: only one design condition, i.e., at cruise flight condition
  Element types: SHELL181 (4-node, linear) or SHELL281 (8-node-quadratic)
  Materials: aerospace-grade aluminum alloy

## Slide 7: Tutorials from Ansys
https://www.youtube.com/watch?v=yiTA2AiswEQ
1
2
3
Pressure loads imported from CFD
Wing deflection
Von Mises stress on the spar and ribs